## Slide 1: Electricity current, Circuits and Schematic Diagrams
Notes: Click on button for story on backyard Tesla coil (YouTube)
Nikola Tesla dreamed of creating a way to supply power to the world without stringing wires across the globe. The inventor came close to accomplishing this when his "mad scientist" experiments with electricity led to his creation of the Tesla coil.
The first system that could wirelessly transmit electricity, the Tesla coil was a truly revolutionary invention.

## Slide 2: Learning Goals:
Elec 2 - I can explain factors influencing current flow and how electrons flow through components in a circuit
Elec 3 – I can describe different types of circuits and draw schematic diagrams showing components and electron flow

## Slide 3
Types of Electricity
Static electricity forms when charges build up and remain on an object for a while.
Current electricity forms when electrons flow through a circuit

## Slide 4
What is Current Electricity?
+
-
http://phet.colorado.edu/en/simulation/travoltage
The flow of negatively charged particles called electrons in a complete circuit.

## Slide 5
Electric current (I) – flow of charge
Amount of charge passing through a set point every second
Higher the current, the faster the electrons move
Unit of measure = amperes (A) or milliamps (mA);
1.0 A = 1000 mA
1 A = 1coulomb/1 second (1 Coulomb is electrons)
Measured with a device called an Ammeter
Analogy: How fast the water in a river flows is like current flow in an electrical cable

## Slide 6: AC Vs DC Circuits
Intro Video EngineeringMindSet
Electric Circuit: A complete pathway that allows electrons to flow from the source and back again.
Record your own notes while viewing videos on Alternating Current vs Direct Current

## Slide 7
Water slide Electric Circuit Analogy
The person represents an electron in a circuit
Stairs are the battery – the source of potential energy (number of stairs is the voltage)
Potential energy lost only when person slides down – like when electrical energy transformed to other forms of energy by a load i.e. light bulb uses electricity to produce light and heat
At bottom electron/person has zero potential energy remaining

## Slide 8
A source such as a battery or solar panel that provides the electrical energy to push electrons through a circuit. The amount of push determines a cells voltage.
Conductor: Wires provide a pathway for the electrons to flow
Load: a device that transforms electrical energy into other forms of energy i.e. motor, light bulb, heater, buzzer
Switch: a device that can stop the flow of electrons by closing or opening a circuit
CIRCUIT COMPONENTS: Four basic parts!

## Slide 9
Electron Flow in a circuit
Electrons flow from –ve to +ve terminals in a closed circuit!
  There are two main types of circuits: Series and parallel circuits
e

## Slide 10: Series: Current has only one pathway through all parts of the circuit.
Series Circuit – Electron flow
Parallel Circuit – Electron flow
Parallel: Current can flow through multiple pathways in the circuit.

## Slide 11: Phet Exploration Activity - insulators vs conductors -circuit components -electron flow in simple circuits -intro to circuit diagrams

## Slide 12: Drawing schematic Diagrams

## Slide 13: Circuit Diagram Examples

## Slide 14: Circuit Diagram Examples
On your own: Draw the schematic diagram
With your partner: Agree on the correct diagram

## Slide 15: Circuit Diagram Examples
On your own: Draw the schematic diagram
With your partner: Agree on the correct diagram

## Slide 16: Circuit Diagram Examples
On your own: Draw the schematic diagram
With your partner: Agree on the correct diagram

## Slide 17: COMPLETE THE HANDOUTs on drawing Circuit Diagrams