## Slide 1: Ohm’s Law
V = I R
Georg Ohm

## Slide 2: How is voltage related to current?
The amount of current that flows through a wire depends on the voltage. The greater the voltage the faster the charges flow.
V = IR
If ↑ V then ↑ I
If ↓ V then ↓ I

## Slide 3: How is Current related to Resistance?
Amount of current also depends on how the wire resists the flow of the charge.
V = IR or I =
If ↓ R then ↑ I
If ↑ R then ↓ I

## Slide 4: Summary - Last slide before notes on Ohm’s Law Calculations
The unit for resistance is called the Ohm (Ω)
The relationships between voltage(V), current(I), and resistance(R):
V = I R
in Volts (V)
in Amperes (A)
in Ohms (Ω)

## Slide 5: DO THIS!
Textbook pages 293, 294 #1-3 on both!
Text: Pg. 301 #8 – 13 (omit 11)
Text: Pg. 303 #26 – 31 (omit 30)
Calculating Resistance Problems! For marks!

## Slide 6: Warm –up use Ohm’s Law V=IR to complete Table By Finding unknown in each row. Show Steps! Convert using conversion factors where needed!
I (amps) | V (volts) | R (ohms)
I= ? A | 12 V | 75 Ω
15 A | 0.24 kV Volts? | R=? Ω
5500 mAAmps? | V=? V | 20

## Slide 7: Ohm’s Law Problem
A vacuum cleaner is plugged into a 120 V outlet. The vacuum cleaner is rated at 12000 mA. What is the resistance of the motor and circuitry of the vacuum?

## Slide 8: Key – Warm-up Ohm’s Law
I (amps) | V (volts) | R (ohms)
I=V/R =12/75 =  =0.16 A | 12 V | 75 
15 A | Convert 0.24 kV  Volts #V = | R=V/I =240/15 = =16 
Convert 5500 mA  Amperes #A = | V=IR =5.5 A x 20  =110 V | 20 
I (amps) | V (volts) | R (ohms)
 | 12 V | 75 
15 A |  | 
 | V=IR =5.5 A x 20  =110 V | 20 

## Slide 9: Doing the Work
Identify the known variables.
Identify all the unknown variables.
Adjust formula to solve for unknown.
Convert all values to standard units. Volts (V)–Ohms () - Amperes(A)
Substitute the numbers into the formula and solve.
Thinking Steps
Voltage (V) = 120 V Current (I) = 12000 mA
Resistance (R) = ?
V = IR 
12000 mA X = 12 A